## Slide 1
Giovanna De Chiara
Satellite information on the ocean surface: Scatterometer, Altimeter and SMOS
7 April 2017
with contributions from Saleh Abdalla, Magdalena Balmaseda, Hao Zou, Patrick Laloyaux, Cristina Lupu,
Nicolas Reul (Ifremer)

## Slide 2
Scatterometer Winds
The importance of scatterometer wind observations
Scatterometer principles
Data usage at ECMWF and their impact
How we can improve usage and impact
Altimeter Wind, Waves, Sea Surface Height
Altimeter principles
Use of altimeter data in the wave and ocean models
Altimeter data impacts
SMOS winds
Principles
Database available
TC examples
Outline

## Slide 3
Why is Scatterometer important?
The scatterometer measures the ocean surface winds (ocean wind vector).
Ocean surface winds:
affect the full range of ocean movement
modulate air-sea exchanges of heat, momentum, gases, and particulates
direct impact on human activities
Wind observations below 850 hPa
FSO values relative quantities (in %)
Wide daily coverage of ocean surface winds
[Horanyi et al., 2013]
Ex: 1 day of ASCAT-A data

## Slide 4
A Scatterometer is an active microwave instrument (side-looking radar)
  Day and night acquisition
  Not affected by clouds
The return signal, backscatter (σ0 sigma-nought), is sensitive to:
  Surface wind (ocean)
  Soil moisture (land)
  Ice age (ice)
Scatterometer
Scatterometer was originally designed to measure ocean wind vectors:
  Measurements sensitive to the ocean-surface roughness due to capillary gravity waves generated by local wind conditions (surface stress)
  Observations from different look angles: wind direction
Returned
Incoming
Notes: Return signal is the collective interference from the total footprint
Scatterometers are active radar instruments and therefore both emit and receive microwave radiation. This radiation has the advantage of not being affected by clouds and this is why scatterometers are known to be able to scan the surface in almost all weather conditions.
  Pulse scattereded depending on the ocean roughness
  Surface roughness (capillary waves ) depends on the wind stress
  Strenght to return to the satellite gives wind stress and direction
COMMENTO PATRICK: fare riferimento ad Alain o Tony che avranno gia spiegato un active and passive sensor

## Slide 5: Scatterometer
The amount of backscatter depends on:
The frequency and polarization of the emitted wave
Backscatter highly depends on:
Wind speed
Relative direction between the surface wind and look angle
  Incidence angle
C-band (5.3 GHz): λ ~ 5.6 cm
Ku-band (14.6 GHz): λ ~ 2.1 cm
Bragg scattering occurs from the ocean capillary-gravity waves (cm-range) that are in resonance with the microwaves
Notes: Over the ocean, the radar backscatter results from scattering from wind-generated capillary-gravity waves, which are generally in equilibrium with the near-surface wind over the ocean. The scattering mechanism is known as Bragg scattering, which occurs from the waves that are in resonance with the microwaves.
  What it actually sees is wave directions generated by local winds…hence the wind direction
curs from the waves that are in resonance with the microwaves.

## Slide 6
Dependency of the backscatter on... Wind speed
Notes: The radar signal is attenuated by the rain as it travels to and from the Earth’s surface  σ0
Some of this scattered energy returns to the instrument  σ0
  Retrieved wind speed ( to ~ 15 m/s)
  Directional information can be lost
ASCAT emits microwave radiation with a wavelength of 5.7 cm. This radiation is resonant with centimeter-scale ocean waves of comparable wavelength due to the so-called Bragg scattering mechanism, and is sent back to the sensor. This backscatter radiation coming from the water surface can then be processed in order to compute near-surface ocean wind speed and direction.
This capability relies on the assumption that the small-scale ocean waves responsible for the backscatter are in equilibrium with the wind. As wind speed increases, surface roughness also increases and more microwave radiation is scattered towards the direction of the radar source

## Slide 7
upwind
downwind
crosswind
Dependency of the backscatter on... Wind direction
upwind
downwind
Wind direction wrt Beam
  Asymmetry Upwind – Downwind (particularly small)
  Asymmetry Upwind – Crosswind
Notes: As shown in Fig. 1.3 the σ0 triplets with the same wind speed lie on the two circumferences, one for upwind and the other for downwind. We can
represent the σ0 measures and the CMOD4 model for the same wind speed projected on the plane
The colour changes around the circumference showing the changes in wind direction; each colour shade indicates 10° of direction. The colour
black is centred on 0°, then passing by the purple we arrive on the blue in 90°. The sky-blue is for 180°, the green for 270°.
The three σο measurements (σο triplet) are uniquely related to the 10 m vector wind through the GMF (Geophysical Model Function. The wind inversion is based on a search for minimum distances between the measured σο triplet and all the backscatter model solutions lying on the GMF surface, taking into account instrumental and geophysical noise sources . Due to measurement noise, multiple solutions are usually found (wind ambiguities), which have to be filtered out using the background wind information provided by a NWP model (ambiguity removal).
COMMENTO PATRICK: parlare piu lentamente, cercando di ripetere piu volte, spiegare perche abbiamo piu colori nel plot o possibilmente rimuovere piu colori.

## Slide 8
Dependency of the backscatter on... Wind direction
Backscatter response depends on the relative angle between the pulse and capillary wave direction (wind direction)
Fore Beam
Mid Beam
Aft Beam
Wind direction wrt Mid Beam
Wind direction wrt Mid Beam
Wind direction wrt Mid Beam
Mid
Fore
Aft
C-band SCAT geometry
Notes: σ0 with respect to the wind direction for mid (top), fore (centre) and aft (bottom) beam for node 10. Each wind speed is plotted with different colours. For the model, plotted with the lines, the speeds of 8, 9 and 10 m/s are reported, for data measurements, plotted with points,all speeds from 8 to 10 m/s.
ince the cm-scale ocean roughness is aligned with wind direction, the radar backscatter depends on the the pointing direction of the radar beam with respect to the wind direction. As such, the radar backscatter depends on both wind speed and wind direction, i.e., on the wind vector.
As a reference it can be stated that Bragg scattering dominates for incidence angles between 25 and 80º, which clearly covers the range of incidence angles for ASCAT.
The wind retrieval algorithm relies on the observation of the same ocean area from different perspectives (different azimuth and incidence angles).
COMMENTO PATRICK: ok ripetendo piu volte

## Slide 9
How can we relate backscatter to wind speed and direction?
The relationship is determined empirically
Ideally collocate with surface stress observations
In practice with buoy and 10m model winds
Geophysical model functions (GMF) families
C-band: CMOD (currently CMOD5.N)
Ku-band: NSCAT, QSCAT
U10N: equivalent neutral wind speed
: wind direction w.r.t. beam pointing
: incidence angle
p : radar beam polarization
: microwave wavelength
Notes: As shown in Fig. 1.3 the σ0 triplets with the same wind speed lie on the two circumferences, one for upwind and the other for downwind. We can
represent the σ0 measures and the CMOD4 model for the same wind speed projected on the plane
The colour changes around the circumference showing the changes in wind direction; each colour shade indicates 10° of direction. The colour
black is centred on 0°, then passing by the purple we arrive on the blue in 90°. The sky-blue is for 180°, the green for 270°.
The three σο measurements (σο triplet) are uniquely related to the 10 m vector wind through the GMF (Geophysical Model Function. The wind inversion is based on a search for minimum distances between the measured σο triplet and all the backscatter model solutions lying on the GMF surface, taking into account instrumental and geophysical noise sources . Due to measurement noise, multiple solutions are usually found (wind ambiguities), which have to be filtered out using the background wind information provided by a NWP model (ambiguity removal).

## Slide 10
C- band scatterometers
Used on European platforms (1991 onwards):
SCAT on ERS-1, ERS-2 by ESA
ASCAT on Metop-A, Metop-B by EUMETSAT
f~5.3 GHz (λ~5.7 cm)
VV polarization
Three antennae
Pros and cons:
Hardly affected by rain
High quality wind direction (especially ASCAT)
Two nearly opposite wind solutions
Rather narrow swath:
ERS-1/2: 500km
ASCAT-A/B: 2x550km

## Slide 11
Ku-band scatterometers
Used on US, Japanese, Indian and Chinese platforms:
NSCAT, QuikSCAT, SeaWinds by NASA (and Japan)
Oceansat by ISRO
Haiyang-2A by China
RapidSCAT on the ISS
Pros and cons:
Up to four wind solutions (rank-1 most often the correct one)
Broad swath (1,800km)
Affected by rain
Problems regarding wind direction:
  azimuth diversity not good in centre of swath
  outer 200km only sensed by one beam.
f~13 GHz (λ ~ 2.2 cm)
VV and HH polarization:
Two rotating pencil-beams (4 look angles)
OSCAT daily coverage

## Slide 12
Operational usage of scatterometer winds at ECMWF
95 | 96 | 97 | 98 | 99 | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
ERS-1
ERS-2
ERS-2 (Regional Mission Scenario)
QuikSCAT
METOP-A ASCAT
METOP-B ASCAT
Oceansat-2 (OSCAT)
C-Band
Ku Band
(RapidSCAT)
Passive
Monitoring

## Slide 13
Scatterometer assimilation strategy
 | C-band | Ku-Band
Resolution | 25 km | 50 km
σ0 bias correction | √ | -
Wind Inversion | ECMWF | KNMI
Wind Speed bias correction | √ | √
QC – Sea Ice check | √ | √
Rain flag check | - | √
Thinning | 100 km | -
Maximum wind speed assimilated | 35 m/s | 25 m/s
Assigned observation error | 1.5 m/s | 2 m/s
4D-Var | 2 solutions | 1 solution
Assimilated as 10m eq. neutral wind (U&V) | √ | √
Purely quadratic cost function

## Slide 14
Wind Direction Ambiguity removal
At each minimization the solutions are compared to the based on the background
Ambiguities provided
Ambiguities selected
Notes: The final selection is done with the penultimate trajectory. During the last minimization the increments are computed to be added to the penultimate trajectory to compute the 'last trajectory' from where the analysis is taken.

## Slide 15
Scatterometer Temporal Coverage
Assimilation Window: 09 – 21 UTC
ASCAT-A
ASCAT-B

## Slide 16
Background Departure
ASCAT-A Wind speed O-B (Oct ‘16)
Wind speed bias in the Tropics: also due to Ocean Current?

## Slide 17: Forecast Impact (FSOI)
ECMWF operations Cy41r2, March 2016, Global data

## Slide 18
For each storm the min SLP have been detected from the ECMWF model fields
SLP have been compared to observation values (from NHC and JMA)
Statistics based only on cases where ASCAT-A, ASCAT-B and OSCAT passes were available
Dec 2012/ Feb 2013
Impact on Tropical Cyclone FC
G. De Chiara, S. English, P. Janssen and J.-R. Bidlot, “ASCAT ocean surface wind assessment”
ECMWF Technical Memorandum 776, 2016.

## Slide 19
TC Haiyan – CY40R1 2013110712 [Assimilation Window 9 - 21]
1 ASCAT-A obs @ 1pm
Philippines
Is the model able to vertically propagate the information?
Single observation experiments

## Slide 20
00 [09h]
03 [12h]
06 [15h]
09 [18h]
12 [21h]
T1279
Single Observation Experiments (1 ASCAT-A)

## Slide 21
U An Incr @ 18h
U An Incr @ 18h
ML 114
V An Incr @ 18h
Model Levels
137
100
50
ML PL(hPa)
137 ~ 1013
114 ~ 850
96 ~ 500
79 ~ 250
60 ~ 100
137
100
50
N
S
N
Res ~ 16 km
S
Single Observation Experiments (1 ASCAT-A)

## Slide 22
Focus on a specific weather event:
TC Phailin
Bay of Bengal
formed on the 4th October 2013
Argo probe with high-frequency measurements
Temperature measurements at 40-meter depth
Impact of scatterometer data in the CERA system
Impact of scatterometer surface wind data in the ECMWF coupled assimilation system
P. Laloyaux, J-N Thépaut and D. Dee. MWR, 2016
Impact of scatterometer winds …on the ocean parameters

## Slide 23: TC Phailin
Ocean temperature analysis at 40-meter depth (scatterometer data are assimilated)
Coupled analysis with Scatterometer winds is closer to the observations with a stronger cold wake
ASCAT-A
ASCAT-B
OSCAT
Wind measurements from scatterometers (ascending pass, 11 October 2013)
Impact of scatterometer winds …on the ocean parameters

## Slide 24
Temperature difference Scatt – NoScatt
November 2013
Impact of scatterometer winds …on the ocean parameters

## Slide 25
How can we improve usage and impact?
Include dependency from other geophysical quantities such as ocean currents
Stress is related to relative wind
The observation operator should act on relative wind
Accurate ocean current input are needed
10m ASCAT-A wind speed
10m FG wind speed
Improve QC mostly for extreme events
  Because of thinning and QC the strongest winds can be rejected
Test on the observation error, thinning and use of high resolution products
TC Haiyan
Ambiguity removal

## Slide 26
CTRL
VarQC/Thin=4/ObsErr=1.5m/s
HN
VarQC / Thin=2
HN & Thin=2
HN & Thin=2 & Obserr=0.5
TC QC issues
TC KILO – 2015090812
Notes: COMMENTO PATRICK: piu slide come questa

## Slide 27
CTRL
VarQC off
HN 3
Thin =2
HN 3/ Thin 2
TC Patricia: DA 2015102312 UTC - ASCAT @ 17.11

## Slide 28: Scatterometer Concluding remarks
ECMWF has a long experience with scatterometry
Available continuously from 1991 onwards:
GMF development
Monitoring, validation, assimilation, re-calibration
On-going efforts to improve usage and impact
Improve QC
Adapt observation errors, thinning, super-obbing
Include dependency from other geophysical quantities
Use in the Reanalysis
ERS1/2 and QuikSCAT in ERA-Interim
ASCAT-A reprocessed products used in ERA5
Scatterometer observations widely used in NWP
Ocean wind vectors
Positive impact on analysis and the forecast
Global scale and extreme events
Impact on Atmospheric, Ocean and Wave model
Typhoon Haiyan 20131107
ASCAT-A ASCAT-B OSCAT

## Slide 29: Radar Altimeters
Radar altimeter is a nadir looking instrument.
Specular reflection.
Electromagnetic wave bands used in altimeters:
Primary:
Ku-band (~ 2.5 cm) – ERS-1/2, Envisat, Jason-1/2/3, Sentinel-3
Ka-band (~ 0.8 cm) – SARAL/AltiKa (only example)
Secondary:
C-band (~ 5.5 cm) – Jason-1/2/3, Topex, Sentinel-3
S-band (~ 9.0 cm) – Envisat
Sentinel-3
Radar Altimeter (SRAL)
Envisat 1-day coverage
Main parameters measured by an altimeter:
  Significant wave height (wave model)
  Wind speed (used for verification)
  Sea surface height (ocean model)
Notes: Most of the modern radar altimetry missions carry dual frequency altimeters to estimate the impact of the atmosphere on the radar signal (ionospheric impact). The primary (or the only in the case of mono-frequency altimeters) electromagnetic wave frequency is usually Ku-band which has a wavelength of about 2.5 cm (e.g. ERS-1/2, ENVISAT, Jason-1/2/3, and Sentinel-3). The exception is SARAL which implements the Ka-band with a wavelength of about 0.8 cm. The secondary frequency is mainly the C-band with a wave length of about 5.5 cm (e.g. Topex, Jason-1/2/3 and Sen
The typical accuracy of significant wave height of the older generation of radar altimeters is thought to be the maximum of 0.5 m or 10% of wave height in the range of 1 to 20 m, while the wind speed accuracy is between 1.5 and 2 m s−1 (for wind speed in the range of 0 to 20 m s−1). As will be discussed later based on a triple collocation technique, nowadays the accuracy of significant wave height is thought to be 6% of significant wave height, while the error in wind speed is around 1.0 m s−1. tinel-3). ENVISAT used S-band (wave length of about 9 cm) as the secondary frequency.

## Slide 30: How Altimeter Works
surface
Height=∆t/2  c
emitted signal returned signal
a t m o s p h e r e
time
ocean surface
illuminated area
Power of illumination
radar signal
time
power
flat surface
rough surface

## Slide 31: Significant Wave Height (SWH)
time
power
waveform
slope of leading edge  SWH
  SWH is the mean height of highest 1/3 of the surface ocean waves
  Higher SWH  smaller slope of waveform leading edge
  Errors are mainly due to waveform retracking (algorithm) and instrument characterisation.
Notes: The earlier return from the wave crests and the retarded return from the wave troughs lead to a deformation of the return pulse which can directly be related to the significant wave height.

## Slide 32: Surface wind speed
  Backscatter is related to water surface Mean Square Slope (MSS)
  MSS can be related to wind speed
  Stronger wind  higher MSS  smaller backscatter
  Errors are mainly due to algorithm assumptions, waveform retracking (algorithm), unaccounted-for attenuation & backscatter.
amplitude of returned signal  wind speed
time
power
waveform
emitted signal backscatter
Notes: The mean square slope (MSS) of sea surface is defined as the variance of surface slope, which is a key parameter in understanding the air–sea interactions and ocean remote sensing.
Air–sea fluxes of mass, momentum, and heat as well as radar scattering are believed to be significantly correlated with MSS. Many factors including wind speed, wave state, air– sea temperature difference, and intensity of sea surfactant films have impacts on the MSS.
Attenuation  atmospheric wind speed (no impact for C band / small for Ku band / important for Ka)

## Slide 33: Sea Surface Height
Time delay  sea surface height
  Radar signal attenuation due to the atmosphere is caused by:
    Water vapour impact: ~ 10’s cm.
    Dry air impact: ~ 2.0 m
    Correction made using radiometer and model data
time
power
waveform

## Slide 34: Operational Assimilation of SWH (wave model)
Assimilation method for SWH data:
  Data are subjected to a quality control process (inc. super-obbing).
  Bias correction is applied.
  Simple optimum interpolation (OI) scheme on SWH.
  The SWH analysis increments  wave spectrum adjustments…
10 Mar. 2009
Jason-1 Envisat
Jason-2 Envisat
Envisat
8 Jun. 2009
Jason-1 Jason-2 Envisat
1 Apr. 2010
Jason-2 Envisat
7 Apr. 2012
Jason-2
22 Oct. 2003
ERS-2
1 May 1996
ERS-1
15 Aug. 1993
1 Feb. 2006
12 May 2015
Jason-2 Cryosat-2 SARAL
Jason-3 OGDR (from Q4, 2017); Sentinel-3 (~Q4, 2017).
Notes: producing super-observations by averaging of 11-13 consecutive measurements covering a length of about 75 km
All wrong, noisy and questionable measurements are discarded. Bias correction is applied to harmonise the altimeter data with the model counterparts. The OI scheme is applied to the SWH. The analysis increments are translated into adjustments to the wave spectrum by shifting and scaling the model spectrum based on ocean wave growth laws (for wind-sea dominated conditions) or conservation of wave slope (for the swell dominated conditions)

## Slide 35: Impact of one additional altimeter on the SWH analysis [CS & J2] - [J2 only]
Impact of SWH assimilation
Notes: It is clear that the Cryosat-2 data work towards calming the wave field in the Southern Hemispheric (SH) extra-tropics (latitudes lower than -20°) and increasing the waves in the Northern Hemispheric (NH) extra-tropics (latitudes higher than 20°) and in the tropics (latitudes between 20°S and 20°N).

## Slide 36
Altimeter data in the Ocean Model
10cm
30 m
From sea level observation it is possible to infer information on the vertical density structure
SLA = Sea Level Anomaly
Assimilated in the ocean model
SLA
The altimeter measures the range which can be used to determine Sea Surface Height (SSH)
SSH
Notes: SLA= SSH – MDT (Mean Dynamic Topography) [based on the climatology]
Variation of the SLA reflects in
A thermocline is a thin but distinct layer in the ocean in which temperature changes more rapidly with depth than it does in the layers above or below.
In the ocean, the thermocline divides the upper mixed layer from the calm deep water below. fo of the deep ocean variation

## Slide 37
El Nino 2015/2016
SL Anomalies Feb 2016
Lon/Depth Temp anom Feb 2016
Notes: A small perturbation in the surface is propagated into the colum down to 300m

## Slide 38
Sea surface height observations from satellite (i.e. AVISO L3 along track SLA data) are assimilated in ECMWF ocean reanalysis (ORAS4, ORAP5 and ORAS5) system using NEMOVAR.
Satellite data includes observations from ERS-1/2, Envisat, Jason-2/3 and Topex/Poseidon, Altika, HY-2A (Cryosat-2 and Sentinel-3 in the future).
The SLA along track data has very high spatial resolution for the 1 degree “class” of ocean assimilation systems  Features in the data which the model can not represent. This can be dealt with in different ways:
  Inflate the observation error to account for non representativeness of the “real” world in the assimilation system
  Construction of “superobs” by averaging
  Thinning
Operational Assimilation of SLA
Obs SLA 10 days
Model (1 deg) SLA in 10 days
Notes: Observation error is inflated, up to 6 times, close to the coast (distance < 800 km)

## Slide 39
superob
thinning
raw
super-observation is created by averaging SLA value, space/time positions
Thinning is randomly select one observation within each superob-grid
share the same obs number, superob grid and OBE
Operational Assimilation of SLA
Before the assimilation, a thinning or superobbing scheme is normally implemented to avoid over sampling of the satellite observations.
Notes: Raw SLA data is from delayed
AVISO v4 along track data from 19970829-0903 for 5 days. The filtered AVISO along track data has a filter resolution of 65 km and sub-sampling of 14 km.
A model Mean Dynamic Topography (MDT) file is also needed so model background fields can be converted to compare with observations.
For along-track SLA observations, the super-observation scheme as implemented in ORAS4 and ORAP5 has been modified to include a random selection scheme to generate perturbations. SLA observations within the same day and within each superob-grid (~100 km resolution) are randomly selected, with the same OBE as calculated using the superobing scheme (see Mogensen et al. 2012)
ORAS4-ORAp5 superobbing
ORAS5 thinning

## Slide 40: Impact of assimilating altimeter SLA: Time correlation with altimeter SL product
CNTL
NEMOVAR TS
ORAS4 (TS+Alti)
Impact of SLA assimilation
Notes: CTRL: no DA
N TS: only in-situ

## Slide 41: Altimeter Concluding remarks
ECMWF has a long experience with altimetry in the wave model
Available continuously from 1993 onwards:
ERS1/2, Envisat, Jason1/2, Cryosat, Saral…
  Future missions: Jason-3, Sentinel-3,…
  Altimeter wind and wave data are used for:
  Data assimilation
  Error estimation
  Use in reanalyses (assimilation and validation)
  Long term assessments & climate studies
  Monitoring of model performance (inc. model resolution) & Assessment of model changes
  Altimeter sea level anomaly:
  Use for assimilation and validation
  Significant impact for surface and sub-surface ocean
  Importance for reanalysis and climate studies
  Uncertainty from the ensemble members potentially used for model error

## Slide 42
SMOS
SMOS (Soil Moisture and Ocean Salinity) was launched in November 2009
The SMOS synthetic antenna consists of 69 radiometer elements operating at L-band (frequency ~1.4 GHz, λ=21 cm) and distributed along three equally spaced arms, resulting in a planar Y-shaped structure.
In aperture synthesis radiometers, a TB image is formed through Fourier synthesis from the cross correlations between simultaneous signals obtained from pairs of antenna elements.
Multi-angular images of the brightness temperature are obtained over a large swath width (1200 km), with a spatial resolution varying within the swath from 30 km to about 80 km, and with a revisit time of less than 3 days.

## Slide 43
SMOS wind data
L-band is less affected by rain, spray and atmospheric effects than higher mw frequencies (C-band, Ku-band)
There is no saturation at high wind speed like for radars
Sea foam, generated by breaking waves which mainly depends on surface wind strength and sea state development, increases the microwave ocean emissivity

## Slide 44
Whitecaps
Foam streaks
Ocean-Atmosphere Interface in very High Wind speed conditions

## Slide 45
Ocean-Atmosphere Interface in very High Wind speed conditions
Most of the increased surface whitening at & above hurricane force (>33 m/s) is principally
induced by the increased streaks coverage
whitecap coverage is found ~constant above Hurricane force ~4
Holthuijsen et al. JGR 2012

## Slide 46
Passive Remote Sensing of Sea at High winds
High emissivity of foam layers in the microwave region
Advantages
Transparent (almost) to the atmosphere
No saturation
Drawbacks
Affected by rain at frequency > 5 GHz
Low spatial resolution of orbiting instruments ~40-50 km
functional of:
)
ΔT
d-
Emissivity e is function of whitecap coverage
W and thickness

## Slide 47
S.Shen and J. Tenerelli 2007
Rain Anatomy in a hurricane
Rain rate [mm/h]
High winds in Hurricanes are very often associated with High rain rates
Because of the small ratio of raindrop size to the SMOS electromagnetic wavelength (~21 cm), scattering by rain is almost negligible at L-band, even at the high rain rates experienced in hurricanes.

## Slide 48
Increase of the microwave ocean emissivity
with wind speed  surface foam change impacts
This information can be used to retrieve the surface wind speed in Hurricanes:
Principle of the Step Frequency Microwave Radiometer (SFMR)
C-band: => Use multi-frequency C-band channels to separate wind from rain effects
NOAA’s primary airborne sensor for measuring Tropical Cyclone surface
wind speeds since 30 year (Ulhorn et al., 2003, 2007).
Hurricane hunter P-3
Wind speed retrieval in extreme winds : SFMR

## Slide 49
SMOS view of Igor Cat 4 Hurricane Igor 2010

## Slide 50
Development of a SMOS wind speed GMF based on Hwind products in IGOR hurricane
Bilinear L-band dependencies with surface wind speed
Geophysical Model function: Tb=f(wind speed)
C-band
L-band:
0.7K/m/s
for hurricanes
0.3 k/(m/s)
below
Reul Nicolas, Tenerelli Joseph, chapron B, Vandemark Doug, Quilfen Y, Kerr Yann (2012). SMOS satellite L-band radiometer: A new capability for ocean surface remote sensing in hurricanes. Journal Of Geophysical Research-oceans, 117

## Slide 51
Collaboration IFREMER, OceanDataLab & Met Office
Improve high wind speed retrieval algorithms (GMF, rain & wave impacts)
Produce a Global Tropical Cyclone & Extra-Tropical Cyclone storm catalogue &
database from 2010 to now
Comparisons with NWP models & radiometer & scatterometer data
Combine with other observations : AMSR2, WindSat, SMAP, CYGNSS
SMOS+STORM Evolution ESA-STSE project

## Slide 52
Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution
Position of the Storm center at the time of SMOS Aquisition

## Slide 53
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 54
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 55
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 56
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 57
Tasks 2: Detect the useful TC & ETC events in SMOS data: Example of EMILIA
SMOS+STORM Evolution

## Slide 58
A view at the SMOS-STORM 2010-2015 TC database
Data available at http://www.smosstorm.org/
A subset of 320 SMOS swath intercepts with TCs over 2010-2015, free of Radio Frequency Interferences and with pixel distances >150 km from the coast are selected

## Slide 59
North Atlantic SMOS intercepts 2010-2015 TC

## Slide 60
Summary
The SMOS brightness temperature signal (∆TB) is clearly associated with the passage of Tropical Cyclones
Correlations between L-band Tb increase with TC intensity from Cat 1 to Cat 5 was demonstrated
L-band observations provide a first non-atmosphere corrupted view of the ocean surface in extreme conditions=> wind speed retrieval with ~5m/s accuracy
A complete storm database as been generated for the SMOS mission archive:
TC & ETC 2010-now available at http://www.smosstorm.org/
Activities ongoing on the retrieval of important structural surface wind features within hurricanes such as the radius of wind speed larger than 34, 50 and 64 knots.
Research in progress on merging low-frequency radiometer observations in extreme conditions: SMOS+AMSR-2+SMAP +…CYGNSS=> new opportunity to study air-sea interactions in extreme wind conditions: foam & whitecaps properties, ocean response to TC passage, drag coefficient.

## Slide 61
Thanks!!!